FidImage module architecture

Without getting into details of the FID format, which are not fundamental to the operation of Recon, I'll describe here qualitatively what FidImage provides to the user. Essentially, a FidImage object gives volume data in four dimensions:

a number of volumes
per volume, a number a sliees
per slice, a number of PE-lines
per PE line, a number of FE read-outs

Thus, the result of print image.data.shape would be (nvol, nslice, n_pe_true, n_fe_true) (see below for variable name descriptions).

In addition to the volume image array, FidImage also gives any reference volumes taken, as well as any navigator lines. In the case of the former, the dimensions of the array would be
(nvol, nslice, n_nav, n_fe), giving nav lines per slice, per image.

For all arrays, PE lines are reordered, and FE points time-reversed, if appropriate for the scan sequence.

FidImage also loads in run parameters from the procpar file (Varian specific). Information found here includes the dimensions discussed above, the number of reference scans, number of segments, PE times, etc. The procpar aspects are all handled by the parent class ProcParImageMixin, which is itself a subclass of ProcPar, which finally is a read-only dictionary of all the data found in procpar. ProcParImageMixin redefines important data as more intelligible variable names.

FidImage inherits a standard image interface from BaseImage, which contains dimensional information

Summary of FidImage data

class FidImage (BaseImage, ProcParImageMixin)

data:
A rank 4 array containing time-domain data. This array is
dimensioned as data(nvol,nslice,n_pe_true,n_fe_true) where nvol
is the number of volumes, nslice is the number of slices per volume,
n_pe_true is the number of phase-encode lines and n_fe_true is the
number read-out points.

nav_data:
A rank 4 array containing time-domain data for the navigator
        echoes of the image data. This array is dimensioned as
        nav_data(nvol,nslice,nav_per_slice,n_fe_true).

ref_data:
A rank 4 array containing time-domain reference scan data
        (phase-encode gradients are kept at zero). This array is dimensioned
        as ref_data(nslice,n_pe_true,n_fe_true).

ref_nav_data:
A rank 4 array containing time-domain data for the
        navigator echoes of the reference scan data which is dimensioned as
        ref_nav_data(nslice,nav_per_slice,n_fe_true).

nav_per_slice	#number of navigator lines per slice
n_pe	#number of phase-encode lines (includes 2 navigator lines)
n_pe_true	#true number of phase-encode lines in a slice (n_pe_true - navigator lines)
n_fe_true	#number of complex frequency-encode points in a pe-line
n_fe	#number of data points (n_fe * 2)
nslice	#number of slices in a volume
pulse_sequence	#may be 'epi', 'epidw', 'epidw_se', etc
nvol	#number of volumes in the data set
nvol_true	#number of volumes including reference volumes
numrefs	# := nvol_true - nvol